## Slide 1
MINI PROJECT
Joystick-Controlled Servo Scanner with Ultrasonic Obstacle Detection
Embedded Systems | Arduino Uno
Sense → Decide → Act
1. Introduction
This mini project is a joystick-controlled scanning arm. An HC-SR04 ultrasonic sensor is mounted on an SG90 servo motor and everything is controlled by an Arduino Uno. The user steers the sensor from 0° to 180°, or switches to an automatic sweep. When an object comes closer than 15 cm, the servo stops and an LED warns the user. It is a small model of the collision-avoidance systems used in robots and vehicles.
Components used
Arduino Uno
HC-SR04 Sensor
SG90 Servo
Joystick Module
LED + 220Ω
Breadboard
Key features
Manual joystick mode and auto-sweep mode (button on D2)
Automatic stop and LED warning below 15 cm
Powered from one 5V pin through breadboard rails

## Slide 2
2. Objectives
2
Main objectives
To control a servo motor smoothly using a joystick (analog input)
To measure distance with an HC-SR04 ultrasonic sensor
To scan a wide area (0°–180°) by mounting the sensor on a servo
To stop the servo automatically and light an LED when an obstacle is within 15 cm
To provide manual and automatic sweep modes with one push button
To build the circuit on a breadboard with a single 5V supply
Skills covered
Analog input (ADC)
PWM servo control
Digital input and output
Pulse timing for sensing
Expected outcome
A working sensor arm that reacts to obstacles
A prototype of the "sense → decide → act" loop

## Slide 3
3. Problem Statement
3
The problem
Machines and robots must avoid obstacles
Human operators can make mistakes
Wrong moves cause damage or injury
Limitations today
A fixed ultrasonic sensor sees only a narrow cone (about 15–30°)
Obstacles at the sides are missed
Manual control has no safety check
Our solution
Servo turns the sensor to scan 180°
Arduino checks distance continuously
Movement stops automatically and the LED warns the user
Problem statement: To design a low-cost, joystick-controlled scanning system that measures the distance to obstacles with an ultrasonic sensor and automatically stops the motion with a visual warning, so that collisions can be avoided.

## Slide 4
4. Working
4
Joystick
(A0, D2)
Arduino Uno
(controller)
SG90 Servo
(D9)
HC-SR04
on servo arm
LED (D6)
X-axis / button
PWM angle
TRIG D3 / ECHO D4
Step by step
1. Joystick sets the servo angle
2. Sensor sends an ultrasonic pulse
3. Echo time gives the distance
4. Arduino compares it with 15 cm
Button on D2
Toggles manual ↔ auto sweep
Decision logic: if distance < 15 cm → servo STOPS and LED turns ON. It resumes only when distance > 18 cm (hysteresis stops flicker). In manual mode the joystick can still move the arm away from the obstacle.

## Slide 5
5. Concept and Connections
5
Component | Pin | Arduino
Joystick VRx | Analog X | A0
Joystick VRy | Analog Y | A1
Joystick SW | Button | D2
HC-SR04 | TRIG | D3
HC-SR04 | ECHO | D4
LED + 220Ω | Anode | D6
SG90 Servo | Signal | D9
All modules | VCC / GND | 5V / GND rails
Arduino 5V → + rail, GND → − rail. A 470 µF capacitor across the rails steadies the servo supply.
Ultrasonic distance
Distance = (time × 0.0343) / 2 cm
Divide by 2: sound goes out and back
Servo and PWM
50 Hz signal; 1 ms ≈ 0°, 1.5 ms ≈ 90°, 2 ms ≈ 180°
Pin D9 is PWM-capable
Joystick and ADC
Two potentiometers give 0–1023 readings
Centre ≈ 512; a dead zone (450–570) prevents drift

## Slide 6
6. Applications
6
Obstacle-avoiding robots
Scanning sensor chooses a free path
Parking assist
Measures the gap to a wall or car
Robotic arms
Stops when a person enters the path
Radar-style scanners
Sweep builds a map of surroundings
Smart cane
Warns visually impaired users
Warehouse AGVs
Vehicles stop for blocked paths
Similar in industry: car parking sensors, emergency braking, robot vacuums, LiDAR scanners, collaborative robots (cobots), AGVs.

## Slide 7
7. Advantages, Limitations and Future Scope
7
Advantages
Low cost and easy to build
Covers 180° with a single sensor
Manual and automatic modes
Instant visual warning (LED)
Good for learning sensors, PWM and ADC
Limitations
HC-SR04 range is short (about 2–400 cm)
Soft or angled surfaces reflect poorly
Beam is wide and readings are slow
Only one axis of scanning
Servo and sensor share 5V from the Arduino
Future scope
Radar display
Bluetooth / ESP32
LiDAR / ToF sensor
PID speed control
TinyML camera

## Slide 8
8. Conclusion
8
Summary
The project shows the basic loop of every automated system: sensing, processing and acting. A joystick steers an ultrasonic sensor mounted on a servo, and the Arduino stops the motion and lights an LED when an obstacle is too close. Built with simple, low-cost parts on a breadboard, the same principle scales up to robots, vehicles and assistive devices using better sensors and AI.
Key learnings
Interfacing sensors and actuators
Analog and digital I/O
PWM servo control
Decision logic with hysteresis
Repository
Wiring diagram and Arduino code (.ino) are included